TCP/IP Networking and Linux
Daniel “Rugmonster” Givens

---
Goals
Provide you with the basics of the OSI model and how it applies to modern networking
Give an overview of the TCP/IP Protocol Suite
Understand IP Addressing and how to configure an IP address on a Linux system
Define a network segment and how to use Linux routing tools to connect outside a local network
Introduce advanced routing and routing protocols as they apply to Linux

---
The OSI Model
I promise, this is going somewhere.
What is the OSI Model?
Application
Application
The Open Systems Interconnection model defines a networking framework for implementing protocols in seven layers. Control is passed from one layer to the next, starting at the application layer in one station, proceeding to the bottom layer, over the channel to the next station and back up the hierarchy.
Presentation
Presentation
Session
Session
Transport
Transport
Network
Network
Data Link
Data Link
Physical
Physical
Physical Link

---
The OSI Model
I promise, this is going somewhere.
The Application Layer
This layer supports application and end-user processes. This layer provides application services for file transfers, e-mail, and other network software services. Telnet and FTP are applications that exist entirely in the application level.
Application

---
The OSI Model
I promise, this is going somewhere.
The Presentation Layer
The Presentation layer relieves the Application layer of concern regarding syntactical differences in data representation within the end-user systems. MIME encoding, data compression, encryption, and similar manipulation of the presentation of data is done at this layer.
Presentation

---
The OSI Model
I promise, this is going somewhere.
The Session Layer
This layer establishes, manages and terminates connections between applications. The session layer sets up, coordinates, and terminates conversations, exchanges, and dialogues between the applications at each end. It deals with session and connection coordination.
Session

---
The OSI Model
I promise, this is going somewhere.
The Transport Layer
This layer provides transparent transfer of data between end systems, or hosts, and is responsible for end-to-end error recovery and flow control. It ensures complete data transfer.
Transport

---
The OSI Model
I promise, this is going somewhere.
The Network Layer
Performs network routing, flow control, segmentation/desegmentation, logical addressing and error control functions. Routers operate at this layer -- sending data throughout the extended network and making the Internet possible.
Network

---
The OSI Model
I promise, this is going somewhere.
The Data Link Layer
At this layer, data packets are encoded and decoded into bits.
The data link layer is divided into two sublayers: The Media Access Control (MAC) layer and the Logical Link Control (LLC) layer. The MAC sublayer controls how a computer on the network gains access to the data and permission to transmit it. The LLC layer controls frame synchronization, flow control and error checking.
Data Link

---
The OSI Model
I promise, this is going somewhere.
The Physical Layer
The Physical layer defines all the electrical and physical specifications for devices. This includes the layout of pins, voltages, frequencies and cable specifications. It provides the hardware means of sending and receiving data on a physical medium.
Physical

---
The TCP/IP Protocol Suite
TCP/IP is known as a protocol suite since it is actually a collection of multiple protocols, each having a distinct function. Here are some of the most common ones we know and use.
TCP
UDP
Guarantees reliable and in-order delivery of sender to receiver data
Does not provide the reliability and ordering guarantees that TCP does, but faster than TCP
IP
ICMP
ARP
IP is a data-oriented protocol used on a packet switched internetwork. Doesn't make any guarantees on the correctness of the data
Chiefly used to send error messages that a requested service is not available or that a host or router could not be reached
The method for finding a host's hardware MAC address when only its logical IP address is known

---
IP Addressing
You won't understand it until later anyway
What exactly is an IP Address?
192.168.1.10
An IP Address is simply a logical (made-up) address. IPv4 addresses consist of 32 bits with a certain number of bits identifying the network they belong to and the remaining bits identifying the unique host address.
11000000.10101000.00000001.00001010

---
IP Addressing
You won't understand it until later anyway
Network... Host... Huh?
192.168.1.10/24
The network portion of the IP address is defined by a network mask. There are several ways network masks are written, CIDR and decimal. They both denote the same thing, the number of bits within the IP address denote the network. So in our example address 192.168.1.10, if we say the CIDR netmask is /24, the subnet mask is 255.255.255.0.
Host
Network
11000000.10101000.00000001.00001010

---
IP Addressing
You won't understand it until later anyway
Doing the Math...
192
Let's go over figuring out how to get our IP address from binary notation. IP addresses are made up of four octets, called so because each is made up of eight bits. Each bit has a value, starting at 1 on the right, the next value being 2, and so on doubling each time until the eighth bit, which equals 128. If the bit is “turned on”, or 1, then we add the equivalent value. To find the binary notation, you subtract the largest bit value from the decimal notation of that octet that will not product a negative value.
  1 1 0 0 0 0 0 0 = 192
128 64 32 16 8 4 2 1

---
IP Addressing
You won't understand it until later anyway
What the Subnet Mask Good For?
Subnet Masks are used in routing determinations. Routers are responsible for sending traffic between networks, thus, they are only concerned with network addresses. Your computer uses the subnet mask to determine whether the system it needs to connect to is on it's local network or if it needs to be passed on to a router.

---
IP Addressing
You won't understand it until later anyway
Enough Theory Already!
Common Syntax
# ifconfig eth0 192.168.1.10 netmask 255.255.255.0 up
# ifconfig eth0
# ifconfig -a
Network interfaces in Linux are named like so:
/dev/eth0, /dev/eth1, ...
/dev/wlan0, /dev/wlan1, ...
/dev/ppp0, /dev/ppp0, ...
Using the command ifconfig, you can assign a static IP address to a network interface and bring it up or down and check the status of all interfaces or specific ones.

---
IP Addressing
You won't understand it until later anyway
Typical Output
# ifconfig eth0
eth0 Link encap:Ethernet HWaddr 00:09:5B:89:CD:D9
        inet addr:192.168.1.10 Bcast:192.168.1.255 Mask:255.255.255.0
        inet6 addr: fe80::209:5bff:fe89:cdd9/64 Scope:Link
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:24525 errors:0 dropped:0 overruns:0 frame:0
        TX packets:17404 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:28253361 (26.9 MiB) TX bytes:2474264 (2.3 MiB)
        Interrupt:16

---
IP Addressing
You won't understand it until later anyway
Geez Whiz....
# arp
Address HWtype HWaddress Flags Mask Iface
10.20.50.100 ether 00:60:97:7F:56:44 C eth1
10.20.50.1 ether 00:0C:41:F2:39:9E C eth1
arp is used to display and edit the ARP table on your system. This is the mappings of IP address to MAC address. Sometimes, an entry in your ARP table can become corrupted (faulty hardware, changed hardware, etc) and you may need to go in and flush a particular address. That can be accomplished with:
arp -d <ip address or hostname>

---
DNS
Without it, you couldn't get to goatse.cx
Overview
Domain Name Service is used to translate readable names, such as www.google.com to an IP address. It is a hierarchical network of servers containing mappings of names and IP addresses.
Root Servers
.mil
.com
.net
.edu
uwf.edu
aum.edu
af.mil
google.com
yahoo.com
erec.net
cs,aum.edu
eglin.af.mil

---
DNS
Without it, you couldn't get to goatse.cx
Configuration in Linux
DNS is configured in two files on most systems. The first is /etc/resolv.conf. You define your DNS server with the nameserver <server ip>. Here's an example:
/etc/resolv.conf
nameserver 192.168.1.1
nameserver 192.168.1.100
If you are using nsswitch (if there is a file /etc/nsswitch.conf, make sure you have this) you need to tell it to use DNS for name resolution. Look for a line starting with hosts, and make sure it says file, dns at the minimum.

---
Routing
When it just has to get there
Network Segments
A hub or switch, or group of hubs or switches connected together, form a network segment. As long as a group of systems have the same network address and reside on the same network segment, they should be able to talk to each other without any more information than an IP address and subnet mask. They all belong to the same network.
192.168.1.0/24

---
192.168.1.0/24
Routing
When it just has to get there
192.168.1.1
Getting Information Between Networks
Routers are used to get information between networks and each interface of a router must be on a separate network segment. Routers use what is called a routing table to determine paths they will use to deliver a packet.
Intar-web
21.134.26.45
42.116.202.11
24.12.36.121
12.21.156.1
153.26.255.254
12.21.156.0/25
153.26.0.0/16

---
Routing
ISP
When it just has to get there
The Gateway of Last Resort
When a system or router doesn't have a specific route for a network, it utilizes a gateway of last resort. Most people know it as the default gateway or default route.
192.168.1.1
192.168.1.0/24

---
Routing
When it just has to get there
Configuring Simple Routes in Linux
In Linux, we use the route command to edit the routing table, because workstations have routing tables too. Here's an example of adding a default route.
# route add default gw 192.168.1.1
If you have multiple networks you want to setup routes for, you can use a command like the following:
# route add -net 10.20.50.0 netmask 255.255.255.0 gw 192.168.1.2
To delete a specific route, simply change add to del. This works for default routes as well as specific routes.

---
Routing
When it just has to get there
Displaying the Routing Table
    Route is also used to display the current routing table, by executing route with no options
    or flags.
# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
localnet * 255.255.255.0 U 0 0 0 eth1
default 192.168.1.1 0.0.0.0 UG 0 0 0 eth1

---
Routing
When it just has to get there
Advanced Routing with Linux
There is a newer routing utility commonly found on most Linux systems known as iproute2. Here is an overview of some of it's features:
Increased performance over route
Support for IP tunnelling (IPv6-in-IPv4 and GRE tunnels)
Support for split access (multiple providers) and load balancing
Support for “marking” packets used in conjunction with iptables
Rule based routing
Multicast routing

---
Routing
When it just has to get there
Routing Protocols
Routing Protocols are used to dynamically share routing information between routers and aid in path determination.
Common routing protocols include:
Border Gateway Protocol – commonly used for large wide area networks
Routing Information Protocol – a very simple routing protocol, used within networks
Interior Gateway Routing Protocol – Cisco proprietary, used within networks
Open Shortest Path First – a very complex routing protocol, also commonly used within networks

---
Routing
When it just has to get there
Routing Protocols in Linux
A Linux based router can support routing protocols thanks to GNU/Zebra. Anyone who has worked with Cisco's Internetwork Operation System will be familiar with it's interface and operation.
Zebra supports:
BGP
RIPv1, RIPv2 and RIPng
OSPFv2 and OSPFv3
Simple access-lists
Most iproute2 features

---
DHCP
It's easier for the most part
Overview
Most networks today get their network configuration via Dynamic Host Configuration Protocol. With DHCP, a system can get an IP address and subnet mask, routes, DNS information and more with no configuration required on the client side. Most SOHO routers run DHCP servers and more can be done with a host based one.
The Downfall
DHCP only works on local network segments due unless a DHCP relay agent is used. Most high end routers can act as DHCP relay agents, but if you don't have one, you must have a system running all the time on each network segment in order for it to work. Security is another potential issue. It is very easy for someone to access a network if DHCP is used and proper physical and wireless security aren't implemented.

---
DHCP
It's easier for the most part
DHCP on the Client Side
There are several popular DHCP clients in use. Your distribution will determine which one you have and each has it's quirks.
dhclient
dhcpcd
pump
Typically, usage is as simple as command <ifname>.
Example:
# dhclient eth0

---
Conclusion and Questions
It's over!
Thank you for your attention. Please feel free to ask any questions.
After the meeting is over, please post any questions to the PcolaLUG Forums!
(http://www.pcolalug.org/smf/index.php)
Resources:
manpages for ifconfig, arp, route, ip, resolv.conf
Wikipedia (http://en.wikipedia.org/wiki/Main_Page)
Webopedia (http://www.webopedia.com/)
Net3-4 HOWTO (http://www.tldp.org/HOWTO/NET3-4-HOWTO.html)
Linux Advanced Routing and Traffic Control HOWTO (http://lartc.org/)
GNU/Zebra Documentation (http://www.zebra.org/zebra/index.html)